## Slide 1: Final Project BBQ Smoker Temperature IoT
Morgan, David
cscie90 Cloud Computing and the Internet of Things
Harvard University Extension School
Prof. Zoran B. Djordjević

## Slide 2: Overview
Problem Statement and Data Used
Technology and tools used
Software
Demo
Summary Pros/Cons
YouTube links

## Slide 3: Problem
Query two temperature probes simultaneously and publish MQTT message so receiving unit can process and display appropriate color-coded indicator to user, regardless of location.

## Slide 4: Describe Cloud Computing Technology
The transmitter uses a NodeMCU with OneWire and DallasTemp libararies to query temperature readings from two thermometers – one embedded in the cooking meat and one measuring ambient grill temperature – and sends that information via MQTT messages to AWS IoT.
The receiver uses a NodeMCU to pull MQTT messages, process the message, and changes two addressable RGB LEDs to notify user of cooking progress and ambient grill temperature using color-coded visual indicators.
All temperature data is viewable in the AWS IoT portal and can be exported in numerous ways to make it viewable over any web-enabled device.

## Slide 5: Describe Data Set
The data set is nothing more than two short MQTT messages from the transmitter every 15 seconds.
First byte of each message is the sequenced temperature probe (allowing for 10 separate thermometers in one application.
Remaining bytes is the temperature reported by that probe.
Degrees are reported in Fahrenheit
Temperatures are sent from AWS IoT to DynamoDB for storage by using a RULE
Ex – “1 145.29”c

## Slide 6: Describe Code Developed
#include <DeviceIndependentInterfaces.h>
#include <Esp8266AWSImplementations.h>
#include <jsmn.h>
#include <sha256.h>
#include <Utils.h>
#include <keys.h>
#include <OneWire.h>
#include <DallasTemperature.h>
#include <ESP8266WiFi.h>
#include <PubSubClient.h>
NodeMCU temperature projects existed
NodeMCU NeoPixel projects existed
NodeMCU MQTT projects existed (very few of them)
No project existed that combined all three…until now
Code from examples found all over the Internet was pieced together then customized
Libraries imported

## Slide 7: Describe Code Developed
Serial.print("Requesting temperatures...");
sensors.requestTemperatures(); // Send the command to get temperatures
Serial.println("DONE");
for (uint8_t s=0; s < sensors.getDeviceCount(); s++) { // iterate through sensors
// get the unique address
sensors.getAddress(grillTemp, s);
// just look at bottom two bytes, which is pretty likely to be unique
int smalladdr = (grillTemp[6] << 8) | grillTemp[7];
Serial.print("Temperature for the device #"); Serial.print(s);
Serial.print(" with ID #"); Serial.print(smalladdr);
Serial.print(" is: ");
float temp = sensors.getTempFByIndex(s); // declare float for accurate temp
Serial.println(temp);
String pubstring; // declare and build message
static char pubchar[14];
static char tempF[8];
String sensorid;
sensorid = String(s);
dtostrf(temp, 6, 2, tempF); // convert float to string
pubstring = sensorid + ' ' + tempF;
pubstring.toCharArray(pubchar,14); // convert string to char array
client.publish("localgateway_to_awsiot", pubchar);// publish message to MQTT
}
delay(15000); // wait 15 seconds
client.loop();
}
Temperature probing and resultant data needed customized code to convert data types in order to be able to send via MQTT

## Slide 8: Describe Code Developed
void callback(char* topic, byte* payload, unsigned int length) {
for (int i=0;i<length;i++) {
char receivedChar = (char) payload[i];
Serial.print(receivedChar);
message = String(message + receivedChar);
}
Serial.println(message[0]);
Serial.println();
if (message[0] == '0') { // Select grill thermometer and
String msgTemp = message.substring(2); // set grillTemp variable to stripped
grillTemp = msgTemp.toFloat(); // message string
}
else if (message[0] == '1') { // Select meat thermometer and
String msgTemp = message.substring(2); // set meatTemp variable to stripped
meatTemp = msgTemp.toFloat(); // message string
}
// NeoPixel color selections for grillTemp
if ((grillTemp < 225.00) || (grillTemp > 300.00)) { // LED 3 turns red blinking at 300degF
for (int j=0;j<10;j++) { // USDA highest temp for smoking meats
pixels.setPixelColor(2, pixels.Color(0,0,0)); // OR
pixels.show(); // turns red blinking at 225degF or lower
delay(1000); // USDA lowest temp for smoking meats
pixels.setPixelColor(2, pixels.Color(255,0,0));
pixels.show();
delay(1000);
}
}
else if ((grillTemp >= 225.00) && (grillTemp <= 300.00)) {// LED 3 turns green btwn 225-300 degF
pixels.setPixelColor(2, pixels.Color(0,255,0)); // USDA rec. grill temp for smoking meats
}
else { // Failover LED 3 to OFF
pixels.setPixelColor(2, pixels.Color(0,0,0));
}
For the RECEIVER, the entire callback function needed to be customized with new code in order to handle the incoming CharArray and convert it to a float in order to be able to calculate color for the NeoPixels

## Slide 9: Show how to run code
To run the broker (mosquitto running on OSX)
sudo /usr/local/sbin/mosquitto –c /usr/local/etc/mosquitto/mosquitto.conf
/usr/local/sbin/mosquitto --- must include full path to binary in OSX
-c /usr/local/etc/mosquitto/mosquitto.conf --- use custom .conf file
To run the NodeMCUs (transmitter & receiver), upload code and push RESET button
The entire project would run just fine with just these steps, but to enable true IoT capabilities, the AWS IoT configuration must be completed

## Slide 10: Show Results from Run
Two results from running code:
1) The receiver’s LEDs will light up specific colors dependent on the message it receives from the transmitter (through the broker and AWS IoT)
There are two parts to the LEDs – 2 LEDs light up specified colors depending on the temperature of the meat (indicated to the receiver when the MQTT message starts with a ‘0’. The 3rd LED lights up a specified color depending on the temperature of the grill (indicated to the receiver when the message starts with a ‘1’).
2) AWS IoT receives the code, and by using a RULE, pushes the message to DynamoDB, where it is stored for future use (potentially a web app that displays temperatures real-time)

## Slide 11: Summarize
Lessons Learned
  Fully explore ALL security protocols required by AWS before starting a project
Advantages/Disadvantages
  Cheap to build and to operate
  Inexpensive temperature probes purchased off eBay might not be exact
  Runs on batteries, but hardcoded SSID access requires access point to travel with you (tether to smartphone?)
  NodeMCU only allows TLS 1.1; AWS IoT requires TLS 1.2; this requires an MQTT broker to be installed locally to bridge the connection
  Nothing like this exists on the market (that I could find) – a visual indicator that really grabs your attention is needed if you are watching the big game
In your own words –what did you think? Would you recommend this Cloud Computing application?
  Needs a professional housing and an updated OS to allow TLS 1.2 (so the broker isn’t necessary), but yes, I would pay for this device if it had a few upgrades

## Slide 12: YouTube URLs
Two minute (short): https://youtu.be/05Ha-BmNZz0
15 minutes (long): https://youtu.be/W5dAXqlkfok